## Slide 1: CoVisor: A Compositional Hypervisor for Software-Defined Networks
Xin Jin
Jennifer Gossels, Jennifer Rexford, David Walker

## Slide 2: Software-Defined Networking
Centralized control with open APIs
Application
Controller
OpenFlow
Network

## Slide 3: Multiple Management Tasks
Hard to develop and maintain a monolithic application
MAC Learner + Firewall + Gateway + Monitor + IP Router
Controller
OpenFlow
Network

## Slide 4: Modular SDN Applications
Frenetic: composition operators to combine multiple applications
Limitation: need to adopt Frenetic language and runtime system
Frenetic Controller
Firewall
Gateway
MAC
Learner
OpenFlow
Monitor
IP Router
Network

## Slide 5: Frenetic is Not Enough
“Best of breed” applications are developed by different parties
  Use different programming languages
  Run on different controllers
Want to mix-and-match third-party controllers
Firewall
Gateway
MAC
Learner
Monitor
IP Router
Network
POX
Ryu
Floodlight
ONOS
ODL

## Slide 6: Slicing is Not Enough
FlowVisor/Open VirteX: each controller works on a disjoint slice of traffic
Firewall
Ryu
Router
ODL
OR
Packet
Firewall
Ryu
Router
ODL
Packet
But, we want multiple controllers to collaboratively work on the same traffic

## Slide 7: CoVisor: A Compositional Hypervisor for SDN
Provide a clean interface to compose multiple controllers on the same network
Composition of multiple controllers
  Composition operators to compose multiple controllers
Constraints on individual controllers
  Visibility: virtual topology to each controller
  Capability: fine-grained access control to each controller

## Slide 8: Composition of Multiple Controllers
Parallel operator (+): two controllers process packets in parallel
Sequential operator (>>): two controllers process packets one after another
Override operator ( ): one controller chooses to act or defer the process to another controller
Use multiple operators
Monitor
Router
Firewall
Router
Elephant Flow Router
Default Router
Firewall
Monitor
Router

## Slide 9: Constraints on Topology Visibility
Physical
Virtual
Firewall
MAC
Learner
Gateway
IP Router
Ethernet
Island
IP Core
S
G
E
I
Many-to-One
One-to-Many
Create virtual topology with two primitives
Benefits: information hiding, controller reuse, composition

## Slide 10: Constraints on Packet Handling Capability
Protect against buggy or malicious third-party controllers
Constrains on pattern: header field, match type
  E.g., MAC learner: srcMAC(Exact), dstMAC(Exact), inport(Exact)
Constraints on action: actions on matched packets
  E.g., MAC learner: fwd, drop

## Slide 11: CoVisor: A Compositional Hypervisor for SDN
CoVisor
OpenFlow
OpenFlow
Compose/ACL
Devirtualize
MAC
Learner
POX
Firewall
Ryu
Gateway
Floodlight
Monitor
ONOS
IP Router
ODL
S
G
E
I
Ethernet
Island
IP Core
E
G
G
I
I

## Slide 12: Compiling Policy Composition
Policy: a list of rules
Compile policies from controllers to a single policy
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
Priority
Match
Action

## Slide 13: Compiling Policy Composition
Policy: a list of rules
Compile policies from controllers to a single policy
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
?. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)

## Slide 14: Policy Compilation
Policy: a list of rules
Compile policies from controllers to a single policy
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
?. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
?. srcip=1.0.0.0/24  count
?. dstip=2.0.0.0/30  fwd(1)
?. *  drop

## Slide 15: Key challenge: Efficient data plane update
Controllers continuously update their policies
Hypervisor recompiles them and update switches
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
3. dstip=2.0.0.0/26  fwd(2)
0. *  drop
Router
?. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
?. srcip=1.0.0.0/24  count
?. dstip=2.0.0.0/30  fwd(1)
?. *  drop

## Slide 16: Key challenge: Efficient data plane update
Computation overhead
  The computation to recompile the new policy
Rule-update overhead
  The rule-updates to update switches to the new policy
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
3. dstip=2.0.0.0/26  fwd(2)
0. *  drop
Router
?. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
?. srcip=1.0.0.0/24  count
?. dstip=2.0.0.0/30  fwd(1)
?. *  drop

## Slide 17: Naïve Solution
Assign priorities from top to bottom by decrement of 1
3. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
2. srcip=1.0.0.0/24  count
1. dstip=2.0.0.0/30  fwd(1)
0. *  drop
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router

## Slide 18: Naïve Solution
Assign priorities from top to bottom by decrement of 1
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
3. dstip=2.0.0.0/26  fwd(2)
0. *  drop
Router
5. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
4. srcip=1.0.0.0/24, dstip=2.0.0.0/26  count, fwd(2)
3. srcip=1.0.0.0/24  count
2. dstip=2.0.0.0/30  fwd(1)
1. dstip=2.0.0.0/26  fwd(2)
0. *  drop

## Slide 19: Naïve Solution
Assign priorities from top to bottom by decrement of 1
Update
3. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
2. srcip=1.0.0.0/24  count
1. dstip=2.0.0.0/30  fwd(1)
0. *  drop
5. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
4. srcip=1.0.0.0/24, dstip=2.0.0.0/26  count, fwd(2)
3. srcip=1.0.0.0/24  count
2. dstip=2.0.0.0/30  fwd(1)
1. dstip=2.0.0.0/26  fwd(2)
0. *  drop
Computation overhead
Recompute the entire switch table and assign priorities
Rule-update overhead
Only 2 new rules, but 3 more rules change priority

## Slide 20: Incremental Update
Add priorities for parallel composition
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
9+7 = 16. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)

## Slide 21: Incremental Update
Add priorities for parallel composition
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
9+7=16. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
9+0=9. srcip=1.0.0.0/24  count
0+7=7. dstip=2.0.0.0/30  fwd(1)
0+0=0. *  drop

## Slide 22: Incremental Update
Add priorities for parallel composition
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
3. dstip=2.0.0.0/26  fwd(2)
0. *  drop
Router
9+7=16. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
9+3=12. srcip=1.0.0.0/24, dstip=2.0.0.0/26  count, fwd(1)
9+0=9. srcip=1.0.0.0/24  count
0+7=7. dstip=2.0.0.0/30  fwd(1)
0+3=3. dstip=2.0.0.0/26  fwd(1)
0+0=0. *  drop

## Slide 23: Incremental Update
Add priorities for parallel composition
Update
16. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
12. srcip=1.0.0.0/24, dstip=2.0.0.0/26  count, fwd(2)
9. srcip=1.0.0.0/24  count
7. dstip=2.0.0.0/30  fwd(1)
3. dstip=2.0.0.0/26  fwd(2)
0. *  drop
16. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
9. srcip=1.0.0.0/24  count
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Computation overhead
Only compose the new rule with rules in monitor
Rule-update overhead
Add 2 new rules

## Slide 24: Incremental Update
Add priorities for parallel composition
Concatenate priorities for sequential composition
3. srcip=0.0.0.0/2, dstip=3.0.0.0  dstip=2.0.0.1
1. dstip=3.0.0.0  dstip=2.0.0.2
0. *  drop
Load Balancer
Router
1. dstip=2.0.0.1  fwd(1)
1. dstip=2.0.0.2  fwd(2)
0. *  drop
.
srcip=0.0.0.0/2, dstip=3.0.0.0  dstip=2.0.0.1, fwd(1)
.
.
3 >> 1 = 25,
011
001
High
Bits
Low
Bits

## Slide 25: Incremental Update
Add priorities for parallel composition
Concatenate priorities for sequential composition
3. srcip=0.0.0.0/2, dstip=3.0.0.0  dstip=2.0.0.1
1. dstip=3.0.0.0  dstip=2.0.0.2
0. *  drop
Load Balancer
Router
1. dstip=2.0.0.1  fwd(1)
1. dstip=2.0.0.2  fwd(2)
0. *  drop
25. srcip=0.0.0.0/2, dstip=3.0.0.0  dstip=2.0.0.1, fwd(1)
9. dstip=3.0.0.0  dstip=2.0.0.2, fwd(2)
0. *  drop

## Slide 26: Incremental Update
Add priorities for parallel composition
Concatenate priorities for sequential composition
Stack priorities for override composition
1. srcip=1.0.0.0, dstip=3.0.0.0  fwd(3)
Elephant Flow Router
Default Router (Max priority = 8)
1. dstip=2.0.0.1  fwd(1)
1. dstip=2.0.0.2  fwd(2)
0. *  drop
1 + 8 = 9. srcip=1.0.0.0, dstip=3.0.0.0  fwd(3)
1. dstip=2.0.0.1  fwd(1)
1. dstip=2.0.0.2  fwd(2)
0. *  drop

## Slide 27: CoVisor: A Compositional Hypervisor for SDN
CoVisor
OpenFlow
OpenFlow
Compose/ACL
Devirtualize
MAC
Learner
POX
Firewall
Ryu
Gateway
Floodlight
Monitor
ONOS
IP Router
ODL
S
G
E
I
Ethernet
Island
IP Core
E
G
G
I
I

## Slide 28: Compiling One-to-Many Virtualization
G
E
I
S
Physical
Virtual
E1
E2
G1
G2
I1
I2
Symbolic path generation
Sequential composition
*
E1
E2
G1
E2
G2
I2
I1

## Slide 29: Compiling One-to-Many Virtualization
G
E
I
S
Physical
Virtual
E1
E2
G1
G2
I1
I2
Symbolic path generation
Sequential composition
Priority augmentation
*
S1
S2
S3

## Slide 30: Implementation and Evaluation
Project website: http://covisor.cs.princeton.edu
  Code, tutorial, etc.
Evaluation
  Parallel composition: L2 Monitor + L2 Router
  Sequential composition: L3-L4 Firewall >> L3 Router
  Topology virtualization: gateway between an Ethernet island and an IP core

## Slide 31: Parallel Composition: L2Monitor + L2 Router
  Compilation time of inserting one rule to L2 Monitor Policy
Chart: L2 Router Policy Size
| 1k | 2k | 4k | 8k | 16k | 32k
Strawman | 80.5287 | 169.055 | 341.3766 | 675.097 | 1492.9542 | 3632.308
CoVisor | 0.001705 | 0.00159 | 0.001807 | 0.002056 | 0.00234 | 0.00246

## Slide 32: Parallel Composition: L2Monitor + L2 Router
  Rule-update overhead of inserting one rule to L2 Monitor Policy
Chart: L2 Router Policy Size
| 1k | 2k | 4k | 8k | 16k | 32k
Strawman | 2007 | 2009 | 2009 | 2009 | 2009 | 2009
CoVisor | 1 | 1 | 1 | 1 | 1 | 1

## Slide 33: Conclusion
CoVisor is a compositional hypervisor for software-defined networks
Provide a clean interface to compose multiple controllers on the same network
For more, visit http://covisor.cs.princeton.edu
Ongoing work: integrate into ONOS with ON.LAB

## Slide 34: Thanks!