## Slide 1
SoftCell: Scalable and Flexible Cellular Core Network Architecture
Xin Jin
Princeton University
Joint work with Li Erran Li, Laurent Vanbever, and Jennifer Rexford

## Slide 2: Cellular Core Network Architecture
access
core
Packet Data Network Gateway
Serving Gateway
Internet
Serving Gateway
Base Station (BS)
User Equipment (UE)

## Slide 3: Cellular core networks are not flexible
Most functionalities are implemented at
Packet Data Network Gateway
  Content filtering, application identification,
  stateful firewall, lawful intercept, …
This is not flexible
Packet Data Network Gateway
Combine functionality from different vendors | 
Easy to add new functionality | 
Only expand capacity for bottlenecked functionality | 

## Slide 4: Cellular core networks are not scalable
access
core
Packet Data Network Gateway
Serving Gateway
Internet
Serving Gateway
Base Station
User Equipment
A lot of processing and state!

## Slide 5: Cellular core networks are not cost-effective
access
core
Packet Data Network Gateway
Serving Gateway
Internet
Serving Gateway
Base Station
User Equipment
Capex & Opex

## Slide 6: Can we make cellular core networks like data center networks?
✔ Flexible
✔ Scalable
✔ Cost-Effective

## Slide 7: Can we make cellular core networks like data center networks?
✔ Flexible
✔ Scalable
✔ Cost-Effective
Yes! With SoftCell!

## Slide 8: SoftCell Overview
No change
Internet
No change
Controller
Commodity hardware
+ SoftCell software

## Slide 9: subscriber attributes + application type  an ordered list of middleboxes
Service Policy:
IPS <-> Firewall
Government Customer
Normal Customer
Firewall
Normal Customer
Parental Control
Content Filter <-> Firewall
“Gold Plan” Customer
Web Accelerator <-> Customized Firewall
Web Traffic
Challenge: Scalable Support of
Fine-Grained Service Policies

## Slide 10: subscriber attributes + application type  an ordered list of middleboxes
Service Policy:
Challenge: Scalable Support of
Fine-Grained Service Policies

## Slide 11: Challenge: Scalable Support of Fine-Grained Service Policies
Packet Classification: decide which service policy to be applied to a flow and tag flows
  How to classify millions of flows?
Traffic Steering: generate switch rules to implement paths for service policy
  How to implement million of paths?

## Slide 12: “North south” Traffic Pattern
Low traffic volume
Small number of active flows
High traffic volume
Huge number of active flows
Too expensive to do packet classification at Gateway Edge!
Access Edge
Internet
Gateway Edge
~1K UEs
~10K flows
~1 – 10 Gbps
~1 million UEs
~10 million flows
~400 Gbps – 2 Tbps

## Slide 13: “North south” Traffic Pattern
Access Edge
Internet
Gateway Edge
~1K UEs
~10K flows
~1 – 10 Gbps
~1 million UEs
~10 million flows
~400 Gbps – 2 Tbps
Opportunity: Traffic initiated from the access edge!

## Slide 14: Asymmetric Edge: Packet Classification
Internet
Access Edge
Gateway Edge
Packet Classification
software
Encode classification results in srcIP and srcPort
Simple Forwarding
hardware
Classification results are piggybacked in dstIP and dstPort

## Slide 15: Challenge: Scalable Support of Fine-Grained Service Policies
Packet Classification: decide which service policy to be applied to a flow and tag flows
  How to classify millions of flows?
Traffic Steering: generate switch rules to implement paths for service policy
  How to implement million of paths?

## Slide 16: Traffic Steering
Steering traffic through different sequences of middlebox instances
  Difficult to configure with traditional layer-2 or layer-3 routing
  [PLayer’08] use packet classifiers, large flow table
What about use a tag to encode a path?
  Aggregate traffic of the same path
  Suppose 1000 service policy clauses, 1000 base stations
  May result in 1 million paths, need 1 million tags
Limited switch flow tables: ~1K – 4K TCAM, ~16K – 64K L2/Eth
Solution: multi-dimensional aggregation

## Slide 17: Multi-Dimensional Aggregation
Use multi-dimensional tags rather than flat tags
Exploit locality in the network
Selectively match on one or multiple dimensions
  Supported by TCAM in today’s switches
Policy Tag
BS ID
UE ID
Aggregate flows going to the same UE
Aggregate flows going to the same (group of) base stations
Aggregate flows that share a common policy (even across UEs and BSs)

## Slide 18: Multi-Dimensional Aggregation
Use multi-dimensional tags rather than flat tags
Exploit locality in the network
Selectively match on one or multiple dimensions
  Supported by TCAM in today’s switches
Policy Tag
BS ID
UE ID
Aggregate flows going to the same UE
Aggregate flows going to the same (group of) base stations
Aggregate flows that share a common policy (even across UEs and BSs)

## Slide 19: Route to different MBs with policy tag
Example service policy clause:
Traffic of this policy is pushed tag1
Match | Action
tag1 | Forward to Filter
SW 2
SW 3
SW 1
Content Filter
Firewall
Match | Action
tag1 | Forward to Firewall
Normal Customer
Parental Control

## Slide 20: Multi-Dimensional Aggregation
Use multi-dimensional tags rather than flat tags
Exploit locality in the network
Selectively match on one or multiple dimensions
  Supported by TCAM in today’s switches
Policy Tag
UE ID
Aggregate flows going to the same UE
Aggregate flows that share a common policy (even across UEs and BSs)
BS ID
Aggregate flows going to the same (group of) base stations

## Slide 21: Location-Based Hierarchical IP Address
BS 1
BS 2
BS 3
BS 4

## Slide 22: Location-Based Hierarchical IP Address
BS ID: an IP prefix assigned to each base station
BS 1
BS 2
BS 3
BS 4
10.0.0.0/16
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16
10.1.0.7
192.168.0.5
UE ID
BS ID
UE ID: an IP suffix unique under the BS ID

## Slide 23: Route to different BSs with BS ID
Forward to base station with prefix matching
Can aggregate nearby BS IDs
10.0.0.0/16
10.1.0.0/16
BS 1
BS 2
Match | Action
10.0.0.0/16 | Forward to BS 1
10.1.0.0/16 | Forward to BS 2
Match | Action
10.0.0.0/15 | Forward to Switch 3
SW 4
SW 3
SW 2
SW 1

## Slide 24: Multi-Dimensional Aggregation
Use multi-dimensional tags rather than flat tags
Exploit locality in the network
Selectively match on one or multiple dimensions
  Supported by TCAM in today’s switches
UE ID
Aggregate flows going to the same UE
Policy Tag
BS ID
Aggregate flows that share a common policy (even across UEs and BSs)
Aggregate flows going to the same (group of) base stations

## Slide 25: Multi-Dimensional Aggregation
Use multi-dimensional tags rather than flat tags
Exploit locality in the network
Selectively match on one or multiple dimensions
  Supported by TCAM in today’s switches
Policy Tag
Aggregate flows that share a common policy (even across UEs and BSs)
BS ID
Aggregate flows going to the same (group of) base stations
UE ID
Aggregate flows going to the same UE

## Slide 26: Policy Consistency
UE Mobility: frequent, unplanned
Policy consistency:
  Ongoing flows traverse the same sequence of middlebox instances, even in the presence of UE mobility
  Crucial for stateful middleboxes, e.g., stateful firewall

## Slide 27: Policy Consistency
An ongoing flow traverses stateful Firewall 1 before handoff
  Use 10.0.0.7 (old IP under BS1), go via the old path
New flow can go via stateful Firewall 2
  Use 10.1.0.11 (new IP under BS2), go via the new path
BS 1: 10.0.0.0/16
192.168.0.5
192.168.0.5
Old flow
Old Path
Old Flow
10.0.0.7
New Flow
New Flow
10.1.0.11
New Path
BS 2: 10.1.0.0/16
Firewall 1
Firewall 2
10.0.0.7
10.1.0.11
Handoff

## Slide 28: Multi-Dimensional Identifier Encoding
Encode multi-dimensional identifiers to source IP and source port
Return traffic from the Internet:
  Identifiers are implicitly piggybacked in destination IP and destination port
Commodity chipsets (e.g., Broadcom) can wildcard on these bits
Policy Tag
BS ID
UE ID
Src IP
Src Port
BS ID
UE ID
Tag
Flow ID
Encode

## Slide 29: Scalable Data Plane Summary
Steering Fabric
Packet classification
Encoding results to packet headers
Traffic steering
Selectively multi-dimensional aggregation
Simple forwarding
Based on encoded multi-dimensional tags

## Slide 30: SoftCell: Scalable and Flexible Cellular Core Network Architecture
Scalable Data Plane
  Asymmetric Edge: Packet Classification
  Core: Multi-Dimensional Aggregation
Scalable Control Plane
  Hierarchical Controller

## Slide 31: Control Plane Load
Internet
Packet classification
Handle every flow
Frequent switch update
Multi-dimensional aggregation
Handle every policy path
Infrequent switch update

## Slide 32: Hierarchical Controller
Controller
Internet
LA
LA
LA
LA
Local agent (LA) at each base station
Offload packet classification to local agents

## Slide 33: Implementation
Controller (Floodlight)
Multi-Dimensional
Aggregation
Packet
Classification
Packet
Classification
Local Agent (Floodlight)
Subscriber
Attributes
Packet Classifiers
Switch Rules
For Path Implementation
Topology
Switch Rules For Header Rewriting
Service Policy
~2 million requests/sec
~2 K – 500 K requests/sec
~10 ms to calculate one path. Can pre-compute.

## Slide 34: Network Wide (Controller Load)
214 UE arrivals/s
280 handoffs/s
99.999th percentile
514 active UEs
Per Base Station (Local Agent Load)
Evaluation: LTE workload characteristics
Easily handled by our prototype controller
(Compare with micro benchmark results in previous slide)

## Slide 35: Evaluation: Data plane scalability
1.7 K rules
for 1 K service policy clauses
13.7 K rules
for 8 K service policy clauses
Commodity switches can handle several K service policy clauses

## Slide 36: Conclusion
SoftCell uses commodity switches and middleboxes to build flexible cellular core networks
SoftCell achieves scalability with
Data Plane
Control Plane
Asymmetric Edge Design for Packet Classification
Multi-dimensional Aggregation for Traffic Steering
Hierarchical Controller Design

## Slide 37: Thanks!

## Slide 38: Related Work
Cellular network architecture:
  [OpenRoads’10]: slice the network to enable multiple carriers
  [Ericsson’12]: GTP tunnel support in OpenFlow
Traffic Steering/Service Chaining:
  [PLayer’08]: use off-path MBs to make it more flexible
  NFV (Network Function Virtualization): virtualize network functions/services, supported by many carriers and vendors
No previous works present a scalable architecture that supports fined-grained policies